Contract for the Supply, Delivery, Testing and Commissioning of Brand New Underwater Breathing Apparatus, Gears and Accessories for the Port Management Office of Misamis Oriental/Cagayan de Oro (PMO MO/C)

TERMS OF REFERENCE

This Terms of Reference (TOR) sets out the guidelines for the procurement including the technical specifications of the above-stated goods.

A.       BACKGROUND

Under P.D 857, as amended, PPA is tasked to undertake the planning, development, financing, construction and operation of ports throughout the country. Incidental to such mandate is to continually assess and regularly  conduct inspections as to the physical conditions of the said ports, berths and wharfs to determine their engineering dependability and integrity after the passage of time, particularly the underwater structures to ensure operational safety and viability. Thus, the Port Management Office of Misamis Oriental/Cagayan de Oro (PMO MO/C) pursuant to ISO-QMS 9001:2008 and PSHEMS, employs various programs and activities to survey the underwater port structure to ascertain the level of engineering maintenance and repair activities to keep the said structures in sound shape.

B.       OBJECTIVE

The PMO MO/C in consonance with the objectives of the ISO-QMS 9001-2008 and PSHEMS,  desires to procure Brand New Underwater Breathing Apparatus, Gears and Accessories to purposely inspect and survey its underwater port structure.

C.      ITEM SPECIFICATIONS

| Lot No. | Item | Technical Description | Unit | Qty. |
| --- | --- | --- | --- | --- |
| 1 | WETSUIT | Full suit 3mm neoprene. Smooth-skin chest and back panels to dry quickly and prevent evaporative heat loss. Smooth skin seals at the neck, arm, and leg openings to seal out water and help keep the body warm. Heavy-duty back zipper with water dam to keep water from rushing in. | sets | 3 |
|  | SCUBA MASK | Lense provide optical clarity and silicone skirt assures precise comfortable fit. • 2 Window Mask with wide Vision lenses • Tempered Glass • Hypoallergenic silicone face skirt and strap | pairs | 3 |
|  | SNORKEL | • Quick release snorkel holder mask strap & easy adjustable snorkel holder. • Clear silicone mouthpiece & clear silicone corrugated flex joint features • with purge valve | pcs. | 3 |
|  | DIVING GLOVES | Suede-like Amara (Synthetic Leather) Palm and Fingers for a high degree of protection, wear resistance and dexterity Adjustable “Hook and Loop” wrist closure | pairs | 3 |
|  | FINS | • Flexible polypropylene blade and thermoplastic rubber foot pocket • open heel type • Blade fitted with a pair of narrow ribs for stability • Rubber side rails have notches about two-third of the way up the blade to increase blade flex • Blade positioned on top of foot pocket board and effective nonskid pattern to combat slippery boat decks | pairs | 3 |
|  | BOOTIES | High-cut 5mm double-glued and blind stitched neoprene construction for longevity and reducing water flow. Razor cut sole for maximum deck grip and flexibility. Reinforced bridge prevents ripping the neoprene when leaning out. | pairs | 3 |
|  | WEIGHT BELTS + BUCKLE | 2lbs high quality weights in Nylon webbing with Stainless steel buckle | pcs. | 3 |
|  | TANK + VALVE | Aluminum 80cf (11.2L) brushed tanks. Minimum burst pressure tested to 2.5 times service pressure without failure. Manufactured to all recognized international standards. Corrosion-resistant interior and exterior, unlike corrosion-prone steel cylinders. Nitrox-ready: cylinders are specially prepared at the factory to be suitable for use with oxygen-enriched air mixtures. Valve designed with an angled handwheel and a shielded side-mounted burst disk safety assembly to make lifting of cylinder easier. Can be used with DIN or Yoke regulators. | tanks | 3 |
|  | UNDERWATER COMPASS | Wrist diving compass, small, sleek, streamlined and durable design. Enhanced readability with prominent pointer in the side-viewing window. High-strength magnet gives fast, positive response. A red lubber line for top-reading accuracy. Abrasion-resistant bezel rotates 360 degrees. | pcs. | 3 |
|  | COMPUTER | Five modes: air, nitrox, gauge, free and off Full continuous decompression algorithm; Built-in dive planner Detailed graphical logs and dive data with your PC/Mac using Suunto DM5 software (cable sold separately as an accessory) Innovative apnea timer for freediving, and a timer in air/nitrox modes Bezel material: Composite Lens material: Acrylic Case material: Composite Strap material: Elastomer Water resistance 120 m (ISO 6425, EN 13319) User replaceable battery Backlight electro-luminescent & phosphor-luminescent Display type matrix Display resolution 49 x 22 Metric and imperial units Maximum operating depth (EN 13319) 80 m Nitrox (and air) Dive time 0 to 999 min Surface time 0 to 99 h 59 min Safety Stop Deep Stop Ascent time display 0 – 199 min (- – after 199) Altitude adjustment 0 – 300 m / 300 -1500 m / 1500 – 3000 m Gases 1 gas (Oxygen 21 – 50%) Gas max pO2 1.2 – 1.6 No-decompression planner Logbook memory ~140 h (20 s sampling rate) Logbook sampling rates 10, 20, 30, 60 s (1, 2, 5 s freediving) | sets | 3 |
|  | SIGNAL BALLOON | ● 210D nylon 48" with 4 mil TPU/ Polyether ● Over pressure release valve ● Inflates with oral valve, low pressure BCD hose, Bottom Duck Bill ● Outer Pouch stores tube when rolled | sets | 3 |
|  | KNIFE | • Made with Titanium Alloy • 4.5" blade with serrations and line cutter • 100% Corrosion Resistant • Pointed Tip Style • Plastic sheath • Titanium butt tank banger for underwater signaling • 2 Rubber Strap included • Anti – Slip Grip | pcs. | 3 |
|  | UNDERWATER TORCH | • Compact, waterproof flashlight with bright, focused beam for maximum distance • 3-position push switch provides full power, 30 percent power and emergency strobe • Powered by three AAA batteries with up to 6 hours of use at full power • Single 230 lumen CREE LED light with a 100,000-hour lifetime • Waterproof to 400 feet; anodized aluminum body | pcs. | 3 |
|  | UNDERWATER CAMERA | Video Resolution: 1080p@60fps Photo Resolution: 12MP, 10MP, 8MP and 5MP Exclusive Video Camera Wide Angle Lens (fisheye) Correction Waterproof rating upgraded to 330 feet / 100 meters (previously 200 feet / 60M) Flat optical-glass lens port with water-repellant & anti-reflection coating Super-wide-angle lens at 160 degrees Digital Zoom: 60x, 16x, 10x or 4x Built-in 1.5” / 3.8cm TFT-LCD 480×240 Rechargeable/Removable Li-ion battery 1150mAh Battery life (approx.): 1.75 hrs (LCD and WiFi off), 1.5 hrs (LCD on and WiFi off), 1.0 hrs (WiFi on and LCD off) Slave strobe function Removable LCD glare hood Diving Mode Motion Detection Mode Time Lapse mode Self-capture mode Burst Mode: 3, 5, 10, 20 and 30 photos Video Rotation Mode (rotate video 180° when camera is mounted upside down) LED indicator-Visual Record Alert front and back High Definition TV output Video codec: H.264 Video format: MP4 / Photo format: JPEG Supports Micro SD Card up to 64GB (class 10 required for HD video recording) | pc. | 1 |
|  | REGULATOR ASSEMBLY AND BCD | Regulator: Balanced First Stage with Pneumatically Balanced 2nd Stage Balanced diaphragm design Large purge button EAN40 (Compatible for Nitrox use up to 40% out of the box) Integrated venturi control extremely efficient exhaust valve Comfo-bite™ mouthpiece Gauge: Clear display of pressure and depth readings for easy viewing under water Dials have a long phosphorescent effect in poor visibility conditions. Provides accurate pressure readings with a range of 360 bar and depth reading range of 70meters Both pressure and depth gauges surpass the EN 250 standard. BCD: Made from tough, advanced fade-resistant Resistek™ material. Increased durability - Robust, with great look with new features Two stainless steel flat D-rings Two large utility pockets are easy to access and will hold all your goodies Right shoulder pull dump with hi-viz orange pull bob Right, lower rear dump with hi-viz orange pull bob The waistband is adjustable and removable Includes chest strap | sets | 3 |

D.      PROJECT SITES

The said goods should be delivered at PMO Bldg. 1, PMO Misamis Oriental/Cagayan de Oro, Port Area, Macabalan, Cagayan de Oro.

E.   APPROVED BUDGET OF THE CONTRACT

The Approved Budget for the Contract (ABC) is FIVE HUNDRED FORTY-SIX THOUSAND EIGHT HUNDRED NINETY-ONE & 18/100 (Php 546,891.18) in Philippine Currency inclusive of 12% VAT. Bids proposed submitted higher than the ABC shall automatically be rejected.

F.    SCOPE OF WORK

- Supply, Delivery, Testing, and Commissioning of Brand New Underwater Breathing Apparatus, Gears and Accessories; and

- Warranty: From the date of delivery of the products, the prospective bidder shall warrant that the products are free from defects in materials and workmanship and shall undertake repair or replacement of any part or portion of the equipment without cost to the government. Warranty period shall not be less than eighteen (18) months.

H.   QUALIFICATION OF PROSPECTIVE BIDDERS

In accordance with Sec. 23.5.1 of the Revised IRR of RA 9184, and the ISO 9001:2008 and PSHEMS Standards currently implemented in this Port, the prospective bidder must possess the following minimum qualifications to be eligible to participate in this public bidding, to wit:

(a)          Duly licensed Filipino citizens/sole proprietorships;

(b)          Partnerships duly organized under the laws of the Philippines, sixty percent (60%) of the interest belongs to citizens of the Philippines;

(c)          Corporations duly organized under the laws of the Philippines, sixty percent (60%) of the outstanding capital stock belongs to citizens of the Philippines;

(d)          Cooperatives duly organized under the laws of the Philippines, sixty percent (60%) of the interest belongs to citizens of the Philippines; and

(e)          Citizens or organizations of a country the laws or regulations of which grant similar rights or privileges to Filipino citizens, pursuant to RA 5183 and subject to Commonwealth Act 138.

I.      TERMS AND CONDITIONS

1.   Prospective bidders must undertake the entire scope of work cited above within 45 calendar days upon receipt of the Notice to Proceed. There shall be only one (1) bid for each participating bidder. No bidder is allowed to submit more than one bid. Otherwise, the bidder shall be disqualified;

2.   Bids submitted after the prescribed deadline on 15 August 2016 at 1:30PM, shall no longer be accepted and considered automatically disqualified;

3.   The Bid Tender/Financial Bid submitted by the bidders shall be inclusive of the 12% Value Added Tax (VAT). However, the VAT and other applicable taxes should be clearly and separately indicated and/or itemized in the bidder’s financial proposal;

4.   Bidders shall submit their respective bids following the prescribed Bidding Forms, and shall comply with the requirements on sealing and marking of bids. Bidders are encouraged to avoid any erasures/modifications on the bid form, otherwise, the said portion shall be duly signed or initialed by the authorized representative of the prospective bidder;

5.  Submitted bids that are not in the prescribed form and/or unsigned shall be considered patently insufficient, and shall be automatically declared non-complying/disqualified.

6.   All prospective bidders are required to submit a bid security in the form and amount prescribed under the revised Implementing Rules and Regulations of RA 9184.

7.   Bidders maybe allowed to withdraw his tender documents before the opening of bids, and the same shall be returned to the bidders unopened. However, no bidder shall be allowed to withdraw his/her offer once and/or after the opening of bids has been conducted or concluded;

8. The bid security shall be returned to the non-winning bidders immediately after the winning bidder has been duly determined and the contract has been awarded, and upon the submission of a letter request for the return of the bid security;

9. The award shall be given to the lowest/single calculated and responsive bid as determined and evaluated by the BAC-PG, and whose bid price is not higher than the ABC;

10. Should there be two or more bidders who submitted the same bid price, BAC-PG shall break the tie in accordance with mechanics provided for under the Government Procurement Policy Board Circular No. 06-2005 dated 05 August 2005;

11. The winning bidder shall not assign or sub-contract or transfer its rights and interest under this contract to any third person, nor shall the same be honored by PPA.

12. All incidental expenses shall be borne solely by the winning bidder;

13. PPA reserves the right to reject any or all bids, to waive any defect in the bids received and to accept such bid which is most advantageous to the Authority.

Recommending Approval:

BIDS AND AWARDS COMMITTEE FOR PROCREMENT OF GOODS:

LEMUEL IAN T. MORALDA                                  MARIA CHONA R. FABIA

Vice- Chairperson                                                   Member

EUTEMIO B. TUMANDA                                       RYAN P. NALZARO

Member                                                                  Member

RUBY MARIA O. GUMAPON

Chairperson

Approved by:

ISIDRO V. BUTASLAC, JR

Port Manager