CONTRACT FOR THE SUPPLY, DELIVERY, INSTALLATION, TESTING, AND COMMISSIONING OF AUTOMATIC IDENTIFICATION SYSTEM (AIS) FOR THE

PORTS OF CAGAYAN DE ORO, BENONI, GUINSILIBAN AND BALINGOAN,

AND AT SULAWAN POINT, ALUBIJID, MISAMIS ORIENTAL, AND TRAINING OF END-USER PERSONNEL

TERMS OF REFERENCE

This Terms of Reference (TOR) sets out the guidelines for the procurement including the technical specifications of the above-stated nature/scope of work for the said units.

A.        BACKGROUND

As of to date, the Port of Cagayan de Oro remains to rely on telephone, radio and email communications for its maritime monitoring and communications. It is not yet covered by any marine traffic AIS network and navigation equipment.

Recognizing the need to modernize and upgrade the ports’ capabilities to monitor vessel traffic movement to improve operational and fiscal efficiency and for other related purposes including disaster preparedness/response, the Philippine Ports Authority has approved the procurement and installation of an Automatic Identification System (AIS) in at least five (5) ports, including the Port of Cagayan de Oro. This project has been enrolled as one of PPA’s commitment to the Governance Commission for GOCCs (GCG) for CY 2016.

B.       OBJECTIVE

The Port Management Office of Misamis Oriental/Cagayan de Oro in its effort to continually improve its port services to its customers, stakeholders and the general public in consonance with the ISO and PSHEMS standards, and in support of PPA’s commitment to GCG, find the necessity to procure and install an Automatic Identification System at the Ports of Cagayan de Oro, Benoni, Guinsiliban, Balingoan and in Sulawan Point in Alubijid, Misamis Oriental in order to enhance vessel traffic movement monitoring in aid of efficient port and harbor management.

C.      PROJECT SPECIFICATIONS

A total of two (2) units AIS Transponder and three (3) units marine traffic AIS Receivers with the following technical specifications shall be supplied, delivered, installed, tested and commissioned at the different project sites cited in Item D, as follows:

Standard Features: ( AIS Transponder)

- Fully satisfies the technical standards for Class-B AIS, IEC 62287-1

- Receives both Class-A and Class-B AIS information

- Enchances safe navigation by exchanging critical navigation information from AIS-equipped vessels nearby

- Greatly improves the level of the situational awareness even in fog, darkness or congested waterways

- Flexible integration with various AIS compatible radar and chart plotters

SPECIFICATIONS

STANDARDS:

IMO MSC.140(76), IEC 62287-1, ITU-R M.1371-2,

DSC ITU R M.825-3, IEC 60945 Ed.4

TRANSPONDER UNIT:

TX/RX Frequency 	156.025 MHz to 162.025 MHz

GPS RECEIVER:

Receiving Channels	12 channels parallel, 12 satellites tracking

Rx Frequency		1575.42 MHz

Rx Code			C/A Code

Position Accuracy	10 m (HDOP<4)

INTERFACE:

COM			RS-422/iec 61162-1

Ethernet			10/100BASE-T

Input:	ACK, BBM, DTM, GBS, GGA, GLL, GNS, HDT, OSD, RMC, SSD,

VBW, VSD, VTG, AIQ, DSC, DSE

Output: 	VDM, VDO, ABK, ACA, ACS, ALR, TXT

POWER SUPPLY:	  12-24 vdc 2.0-1.0 A

ENVIRONMENT:

Temperature

Transponder Unit:  	-15 to +55oC

Antenna Unit:		-30 to +70oC

Waterproofing

Transponder Unit:  	IP20

Antenna Unit:		IPx6

EQUIPMENT LIST:

Standard

1. AIS Transponder

2. GPS Antenna  GPA-0175 or GPS/VHF Compbined Antenna GVA- 100-T with Distribution Box BD-1 (Optional VHF Antenna is needed)

3. Installation Materials and Spare Parts

Standard Features: (AIS Receiver)

- Enhances safe navigation by receiving critical navigation information from local AIS-equipped vessels

- Vastly improves situational awareness in any weather conditions including dense fog, darkness, and congested waterways

- Dual parallel channel, “Full Duplex” receiver design receives AIS contact messages up to 100% more frequently than “Multiplexing” receivers

- High sensitivity, synthesized receiver automatically switches between international and local AIS channels

- Optional amplified VHF splitter allows the use of a single antenna for VHF radio and AIS Receiver

- Serial Output for integration with various radar and chart plotter systems

- Bulkhead mounting and low power, flexible DC input voltage design for simplified installations

- Receives dual frequencies from 156.025MHz to 162.025MHz

- Static Data:

  - MMSI (Maritime Mobile Service Identity)

  - IMO number

  - Ship's name

  - Call sign

  - Length and beam

  - Type of ship

  - Location of position-fixing antenna on the ship

- Dynamic Data:

  - Coordinated universal time (UTC)

  - Course over ground (COG)

  - Speed over ground (SOG)

  - Heading

  - Navigation status*

- Voyage Related Data:

  - Ship's draft*

  - Hazardous cargo

  - Destination and ETA*

  - Safety-related messages

- Alert:

  - LED display

  - Serial data output

STANDARDS REFERRED:

IMO Res. MSC.74 (69) Annex 3, ITU-R Rec. M.1371-2

IEC 61993-2 Ed.1 (Class-A AIS), IEC 62287-1 (Class-B CS-TDMA AIS),

IEC 60945 Ed.4, IMO Res. A.917 (22)

RECEIVING UNIT:

RX Frequency 156.025 MHz to 162.025 MHz

Channel Spacing 25 kHz/12.5 kHz

INTERFACE:

NMEA0183

Input: ACK, ACA, AIQ, DTM, GBS, GGA, GLL, GNS, HDT, OSD, RMC, VBW, VTG, DSC, DSE, ZDA, PFEC

Output (38.4kbps): VDM, VDO, ACA, ACS, ALR, TXT

Ethernet 10/100BASE-T

POWER SUPPLY: 12-24 VDC, 1.2-0.6 A

ENVIRONMENT:

Temperature (IEC 60945 Ed.4) -15 to +55 °C

Humidity (IEC 60945 Ed.4) +40 °C, 93%RH

Waterproofing (IEC 60529) IP20

EQUIPMENT LIST:

1. AIS Receiver with a Power/Serial combined cable (3 units)

2. AIS Viewer Software (1 set)

3. Installation Materials and Spare Parts (3 sets)

D.       PROJECT SITES

This project includes the supply, delivery, installation, testing and commissioning of AIS Transponder at two (2) identified areas, to wit:

- Port of Cagayan de Oro, Cagayan de Oro City

- Sulawan Point in the Municipality of Alubijid, Misamis Oriental Province

And an AIS Receiver at three (3) identified areas, as follows:

- Port of Benoni, Mahinog, Camiguin Province

2)  Port of Guinsiliban, Camiguin Province

3)  Port of Balingoan, Balingoan, Misamis Oriental Province

E.   APPROVED BUDGET OF THE CONTRACT

The Approved Budget for the Contract (ABC) is ONE MILLION ONE HUNDRED THOUSAND FIVE HUNDRED TEN (Php 1,100,510.00) in Philippine Currency inclusive of 12% VAT. Bids proposed submitted higher than the ABC shall automatically be rejected.

F.    SCOPE OF WORK

- Installation of AIS units shall cover the supply, delivery, installation, testing and commissioning of two (2) AIS Tranponders and three (3) AIS Receivers and its accessories/peripherals at the identified sites. Labor and materials shall include the following;

  - labor (transportation, field allowance, board/lodging and other incidental expenses of technicians);

  - materials (carpentry, welding job and other incidental materials)

- Supply, delivery, installation, testing and commissioning of AIS viewer software;

- Supply, delivery, installation, testing and commissioning of One (1) Complete Set Computer for data storage, viewing and transmission;

- Subscription fees in the aftermarket services (1 year);

- On-site end-user training including basic troubleshooting, with a duration not less than five (5) working days.

- Warranty: From the date of delivery of the products, the prospective bidder shall warrant that the products are free from defects in materials and workmanship and shall undertake repair or replacement of any part or portion of the equipment without cost to the government. Warranty period shall not be less than eighteen (18) months.

G.   TOOLS AND EQUIPMENT REQUIREMENT

The prospective bidder shall commit to provide the minimum tools and/or equipment to be utilized during project implementation.

Provided, the subject tools and/or equipment are wholly owned, or under lease agreement of which the period of the said contract must not be less than duration of the project.

The prospective bidder should exclusively dedicate the aforementioned tools/equipment and personnel/manpower within the entire duration of the contract, or until completion of the project as evidence by the Certificate of Acceptance duly signed by the authorized representative/signatory of PPA-PMO-MOC, whichever comes first.

H.   QUALIFICATION OF PROSPECTIVE BIDDERS

In accordance with Sec. 23.5.1 of the Revised IRR of RA 9184, and the ISO 9001:2008 and PSHEMS Standards currently implemented in this Port, the prospective bidder must possess the following minimum qualifications to be eligible to participate in this public bidding, to wit:

(a)   Duly licensed Filipino citizens/sole proprietorships;

(b)   Partnerships duly organized under the laws of the Philippines, sixty percent (60%) of the interest belongs to citizens of the Philippines;

(c)   Corporations duly organized under the laws of the Philippines, sixty percent (60%) of the outstanding capital stock belongs to citizens of the Philippines;

(d)   Cooperatives duly organized under the laws of the Philippines, sixty percent (60%) of the interest belongs to citizens of the Philippines; and

(e)  Citizens or organizations of a country the laws or regulations of which grant similar rights or privileges to Filipino citizens, pursuant to RA 5183 and subject to Commonwealth Act 138.

I.      TERMS AND CONDITIONS

1.  Prospective bidders must undertake the entire scope of work cited above within 30 calendar days upon receipt of the Notice to Proceed. There shall be only one (1) bid for each participating bidder. No bidder is allowed to submit more than one bid. Otherwise, the bidder shall be disqualified;

2.  It is the responsibility of the participating bidders to coordinate and conduct an on-site inspection of the identified installation sites and to secure a Certificate of Inspection from the Port Manager and/or his duly authorized representative for the Port of Cagayan de Oro, and the Terminal Manager for the Port of Balingoan, Benoni, Guinsiliban and TMO - Opol;

3.  Bids submitted after the prescribed deadline which is August 15, 2016, 8:30AM shall no longer be accepted and considered automatically disqualified;

4.   The Bid Tender/Financial Bid submitted by the bidders shall be inclusive of the 12% Value Added Tax (VAT). However, the VAT and other applicable taxes should be clearly and separately indicated and/or itemized in the bidder’s financial proposal;

5.   Bidders shall submit their respective bids following the prescribed Bidding Forms, and shall comply with the requirements on sealing and marking of bids. Bidders are encouraged to avoid any erasures/modifications on the bid form, otherwise, the said portion shall be duly signed or initialed by the authorized representative of the prospective bidder;

6.   The prospective bidder shall submit to PPA its methodology or procedure to be observed in the installation and commission of the said AIS.

7.   Submitted bids that are not in the prescribed form and/or unsigned shall be considered patently insufficient, and shall be automatically declared non-complying/disqualified.

8.   All prospective bidders are required to submit a bid security in the form and amount prescribed under the revised Implementing Rules and Regulations of RA 9184.

9.   Bidders maybe allowed to withdraw his tender documents before the opening of bids, and the same shall be returned to the bidders unopened. However, no bidder shall be allowed to withdraw his/her offer once and/or after the opening of bids has been conducted or concluded;

10.The bid security shall be returned to the non-winning bidders immediately after the winning bidder has been duly determined and the contract has been awarded, and upon the submission of a letter request for the return of the bid security;

11.The award shall be given to the lowest/single calculated and responsive bid as determined and evaluated by the BAC-PG, and whose bid price is not higher than the ABC;

12. Should there be two or more bidders who submitted the same bid price, BAC-PG shall break the tie in accordance with mechanics provided for under the Government Procurement Policy Board Circular No. 06-2005 dated 05 August 2005;

13. The winning bidder shall not assign or sub-contract or transfer its rights and interest under this contract to any third person, nor shall the same be honored by PPA.

14. All incidental expenses shall be borne solely by the winning bidder including the weighing fees, fees and taxes and other charges;

15. There is no employee/employer relationship between employees of the winning bidder and PPA. Hence, the winning bidder shall solely assume responsibility for the payment of salaries, monetary benefits and such other payment for injuries which may be suffered by its employees while implementing the contract.

16. The winning bidder shall assume full responsibility, be liable and agrees to indemnify PPA, or any party/ies for any loss, damage, destruction and/or injury which are attributable in whole or in part to the negligence, fault, laxities, unlawful act or misconduct of the former and/or through its authorized representative or personnel arising from the performance of the project, or resulting from theft, pilferage, robbery, arson and accidents/incidents. The damages or injuries shall be reported in writing to PPA and/or other parties immediately or within two (2) days from the date of its discovery to enable PPA to investigate the matter. However, the winning bidder is not precluded from pursuing any legal action against the person responsible.

17. PPA reserves the right to reject any or all bids, to waive any defect in the bids received and to accept such bid which is most advantageous to the Authority.

Recommending Approval:

BIDS AND AWARDS COMMITTEE FOR PROCREMENT OF GOODS:

MARIA AMOR G. MANN                   	 MARIA CHONA R. FABIA

Provisional Member                                  Regular Member

EUTEMIO B. TUMANDA                           RYAN P. NALZARO

Regular Member                                        Regular  Member

LEMUEL IAN T. MORALDA

Vice-Chair person

RUBY MARIA O. GUMAPON

Chairperson

Approved by:

ISIDRO V. BUTASLAC, JR

Port Manager