Contract for the Supply, Delivery, Installation, Testing and Commissioning of One (1) Unit 1000KVA Generator Set with Automatic Transfer Switch (ATS)  and 2000 Liters Stainless Day Tank for the Port of Misamis Oriental/Cagayan de Oro

TERMS OF REFERENCE

This Terms of Reference (TOR) sets out the guidelines for the procurement including the technical specifications of the above-stated goods.

A.       BACKGROUND

Under P.D 857, as amended, PPA is tasked to undertake the planning, development, financing, construction and operation of ports throughout the country. Incidental to such mandate is to ensure that port operations are running smoothly 24/7 all throughout the year. As such, continuous power supply is vital to support electrical needs during port operations and to ensure sufficient illumination of the port areas and its facilities, including perimeter fences to protect against any unlawful elements.

Thus, the Port Management Office of Misamis Oriental/Cagayan de Oro (PMO MO/C) pursuant to ISO-QMS 9001:2008, PSHEMS and ISPS Code, ensures provision of vital resources i.e. uninterrupted power supply to support port operations, full operations of its facilities, strengthen security and assure continuous public service.

B.       OBJECTIVE

To provide, install, commission and operate generator set at the Port of Cagayan de Oro to ensure the continuous or uninterrupted supply of electricity/power in the port areas particularly at the Passenger Terminal Buidling/Complex during brown-outs/power outage from local power service provider.

C.      ITEM SPECIFICATIONS

| Lot No. | Item | Technical Description | Unit | Qty. |
| --- | --- | --- | --- | --- |
| 1 | One (1) unit of 1000KVA Generator set with ATS and 2000 Liters Stainless Day Tank | Number of cylinders: 12 Cylinder arrangement: V-Type Aspiration: Turbocharged after-water cooling Prime Rating Power (kW/kVA): 720kW/900kVA Standby Rating Power (kW/kVA): 800kW/1000kVA Control Panel: Digital Speed governor: Electrical Cooling system: Water Cooling Cycle Phase : 3 Rpm : 1800 Volts: 230Vac Frequency: 60Hz Power Factor: 0.8 Fuel consumption at 100% load (L/H): 180 Insulation: Class H Starter motor: 24V Exciter type: Single bearing, Brushless, Self-excited Silent Type : Imported Sound Proofed and Weather Proofed Canopy Certification: a. ISO Certified Product b. Red Ribbon Certificate Supplier | set | 1 |

D.   PROJECT SITE

The said goods should be delivered, installed and commissioned at the Passenger Terminal Complex, Port Area, Macabalan, Cagayan de Oro. (Annex “A” & “B”)

E.   APPROVED BUDGET OF THE CONTRACT

The Approved Budget for the Contract (ABC) is TWENTY-FIVE MILLION PESOS (Php 25,000,000.00) in Philippine Currency inclusive of 12% VAT. Bids proposed submitted higher than the ABC shall automatically be rejected.

F.    SCOPE OF WORK

- Mobilization of manpower, materials, tools, equipment and technical supervisions.

- Construction of Concrete Pedestal with shelter. (Annex “C”)

- Supply, Delivery, Installation, Testing, and Commissioning of brand new generator set and all ancillary equipment required for installation and operation.

- Supply and Installation of Cable wires from Generator sets to ATS and Main Distribution Panel.

- Installation of appropriate safety measures at the project site.

- Provisions of warranties:

  - Two (2)-years warranty against manufacturer’s defects from receipt of the Certificate of Acceptance.

  - Three (3) years warranty for parts and services from the date of receipt of the Certificate of Acceptance.

- Actual Load testing before final acceptance.

- Conduct of a one (1) day training for the end-user operator for operating system, commissioning and preventive maintenance procedure.

- Supplier/contractor must secure applicable Permit to Operate with the Department of Environment and Natural Resources (DENR) and Energy Regulatory Commission (ERC) for the said generator set before acceptance.

H.   QUALIFICATION OF PROSPECTIVE BIDDERS

In accordance with Sec. 23.5.1 of the Revised IRR of RA 9184, and the ISO 9001:2008 and PSHEMS Standards currently implemented in this Port, the prospective bidder must possess the following minimum qualifications to be eligible to participate in this public bidding, to wit:

(a)          Duly licensed Filipino citizens/sole proprietorships;

(b)          Partnerships duly organized under the laws of the Philippines, sixty percent (60%) of the interest belongs to citizens of the Philippines;

(c)          Corporations duly organized under the laws of the Philippines, sixty percent (60%) of the outstanding capital stock belongs to citizens of the Philippines;

(d)          Cooperatives duly organized under the laws of the Philippines, sixty percent (60%) of the interest belongs to citizens of the Philippines; and

(e)          Citizens or organizations of a country the laws or regulations of which grant similar rights or privileges to Filipino citizens, pursuant to RA 5183 and subject to Commonwealth Act 138.

(f)	Supplier/contractor must have at least Five (5) years experience in the market of supplying generator set.

(g)	Supplier/contractor must have an employed professional electrical engineer with a valid PRC license.

(h)	Supplier/contractor must have an employed professional Civill engineer with a valid PRC license.

I.      TERMS AND CONDITIONS

1.   Prospective bidders must undertake the entire scope of work cited above within sixty (60) calendar days upon receipt of the Notice to Proceed. There shall be only one (1) bid for each participating bidder. No bidder is allowed to submit more than one bid. Otherwise, the bidder shall be disqualified;

2.   Bids submitted and not received by the BAC-PGS Secretariat after the prescribed deadline on 10 August 2017 at 1:30PM, shall no longer be accepted and considered automatically disqualified;

3.   The Bid Tender/Financial Bid submitted by the bidders shall be inclusive of the 12% Value Added Tax (VAT). However, the VAT and other applicable taxes should be clearly and separately indicated and/or itemized in the bidder’s financial proposal;

4.  Bidders shall submit their respective bids following the prescribed Bidding Forms, and shall comply with the requirements on sealing and marking of bids. Bidders are encouraged to avoid any erasures/modifications on the bid form, otherwise, the said portion shall be duly signed or initialed by the authorized representative of the prospective bidder;

5.  Submitted bids that are not in the prescribed form and/or unsigned shall be considered patently insufficient, and shall be automatically declared non-complying/disqualified.

6.   All prospective bidders are required to submit a Bid Securing Declaration or bid security in the form and amount prescribed under the revised Implementing Rules and Regulations of RA 9184.

7.   Bidders maybe allowed to withdraw his tender documents before the opening of bids, and the same shall be returned to the bidders unopened. However, no bidder shall be allowed to withdraw his/her offer once and/or after the opening of bids has been conducted or concluded;

8. The bid security shall be returned to the non-winning bidders immediately after the winning bidder has been duly determined and the contract has been awarded, and upon the submission of a letter request for the return of the bid security;

9. The award shall be given to the lowest/single calculated and responsive bid as determined and evaluated, and as duly recommended to the HOPE by the BAC-PGS, and whose bid price is not higher than the ABC;

10. Should there be two or more bidders who submitted the same bid price, BAC-PG shall break the tie in accordance with mechanics provided for under the Government Procurement Policy Board Circular No. 06-2005 dated 05 August 2005;

11. The winning bidder shall not assign or sub-contract or transfer its rights and interest under this contract to any third person, nor shall the same be honored by PPA;

12. All incidental expenses shall be borne solely by the winning bidder specifically on the cost of the application of permits from the DENR and ERC, or from other government offices if necessary;

13. PPA reserves the right to reject any or all bids, to waive any defect in the bids received and to accept such bid which is most advantageous to the Authority.

Done this 20th day of July, 2017 at Cagayan de Oro City.

Prepared by:

Technical Working Group

(Original Signed)						(Original Signed)

JONATHAN F. SALIRING		`			ROSY A. DULDOCO

Member							Member

(Original Signed)						(Original Signed)

CHERRYL C. PADILLA					EDSEL A. CALO

Member							Head

Reviewed & Recommend for Approval:

BIDS AND AWARDS COMMITTEE FOR PROCREMENT OF GOODS:

(Original Signed)					    (Original Signed)

LEMUEL IAN T. MORALDA                                  MARIA CHONA R. FABIA

Vice- Chairperson                                                         Member

(Original Signed)					    (Original Signed)

EUTEMIO B. TUMANDA                                       RYAN P. NALZARO

Member                                                              Member

(Original Signed)

RUBY MARIA O. GUMAPON

Chairperson

Approved/Disapproved by:

(Original Signed)

ISIDRO V. BUTASLAC, JR

Port Manager/Head of Procuring Entity (HOPE)