REQUEST FOR QUOTATION

(SMALL VALUE PROCUREMENT)

The Philippine Ports Authority, PMO – NBB, through its Bids and Awards Committee for Procurement of Goods (BAC-PG) will undertake an alternative method of procurement through Shopping for the Supply, Delivery & Commissioning of Construction Equipment at Banago Port, in accordance with Section 52.1 (b) of the Revised Implementing Rules and Regulation of RA 9184.  Interested Bidders/Suppliers are invited to submit price quotations for the following Small Value Procurement of Goods:

- Name of Project	:	SUPPLY, DELIVERY & COMMISSIONING OF CONSTRUCTION

EQUIPMENT

- Location		:	PPA, PMO-NBB, Banago Port, Brgy. Banago, Bacolod City

- Brief Description	:	Supply, Delivery & Commissioning of One (1) Lot Capital Outlay -

Construction Equipment as follows:

| Item No. | Description / Specification | Qty. | Unit | Approved Budget for the Contract |
| --- | --- | --- | --- | --- |
|  | ONE (1) LOT CONSTRUCTION EQUIPMENTS Welding Machine Heavy duty & Industrial type Power Voltage (V) – 220V-240V Digital Amp meter display With Voltage reduction device No-Load Voltage 75 Input Voltage Frequency (Hz) 50/60 Hz Current range (Amp) 500 or more Rated duty cycle - 60 Insulation class - F Protective class - IP21 Power Factor - 0.93 Usable electrodes (mm) 1.6-8.0 Portable Welding Machine Power Voltage – 220V – 240V Rated Input capacity (kVA0 6.3 Input Voltage Frequency (Hz) - 50/60 Hz Current range (Amp) 300 or more Rated duty cycle - 60 Insulation class – F Protective class IP21 Rated input voltage – 220-240V Power factor - 0.93 Net weight (KG) – 4.9 Usable electrodes (mm) 1.6-4.0 Clamp Tester/Meter with Accessories Digital Clamp Multimeter - Badwidth 50-400HZ - Clamp Diameter/conductor size 25mm/ 10 X 30mm or more - Size/mass H187 X W50 X D29mm/ 210g or more Electric Bar Cutter/Cut Off Machine - Cutting fence - Spark deflector for safety - Resistant steel base - Cutting capacity at rectangle - 100 x 196mm Cutting capacity at square – 119 x 119mm Cutting capacity at L-profile – 130 x 130mm Tool dimensions (width x length x height) – 256 x 520 x 400 mm Cutting disc diameter – 355mm Cutting disc bore – 25.4mm Weight – 15 kg Rated Input power – 2,200W Telescopic Ladder - Fiberglass rails in safety orange - Quicklatch rung lock - Outside slide guides - 10-17 Rungs / 20Ft or more - Heavy duty / self-aligning swivel Safety feet with steel ice plate Maximum Load 150g or more Pressure Washer with Accessories - 90bar 1300psi High Pressure washer - Electric water cleaner pump hose - Hose Length 10M or more with handle - Motor power : 1200W - 2HP Copper Oxygen & Acetylene Tank With Welding and cutting outfit - G150-60-540R Oxygen Regulator - G150-15-200R Acetylene Regulator - CA1350 Cutting Attachment - 100FC Torch Handle - MC Acetylene Bottle - 20 cu/ ft. Oxygen Bottle - 12.5” x 3/16” Grade R Twin Hose - 1-W-1 Welding Nozzle - 0-3-101 Cutting Tip - Striker - Goggles - Cylinder Wrench with Chain - Rugged molded plastic carrying case GRAND TOTAL | 1 1 1 1 1 1 1 | Unit Unit Unit Unit Unit Unit Unit | P 148,000.00 |

*Inclusive of 12% VAT

- Delivery Period				 :	Within Ten (10) calendar days from receipt of

Applicable Purchase Order (PO)

- Approved Budget for the Contract (ABC):	P 148,000.00

- Deadline for Submission of RFQ	             :          October 11, 2019 (Friday) - 12:00NN

Please quote your best quotation in line with the above stated specifications.  Suppliers are required to submit their valid current Mayor’s Permit, PhilGeps Registration Certificate, Income/Business Tax Return and Omnibus Sworn Statement.

Quotations may be submitted personally to the BAC Secretariat, PPA Building, Banago Port, Brgy. Banago, Bacolod City or email to zedricturtogo@gmail.com.

For further information, please refer to:

BAC- PG - Secretariat

Philippine Ports Authority, PMO – NBB

Banago Port, Brgy. Banago, Bacolod City

Tel #: (034)441-1225/  441-1041/ 441-3124

Very Truly Yours,

(SIGNED)

RICHIE A. VILLASANA

Chairperson, Bids and Awards Committee