INVITATION FOR SUBMISSION OF QUOTATION

(SMALL VALUE PROCUREMENT)

(RE-POSTING)

The Philippine Ports Authority, Port Management Office of Negros Occidental/Bacolod/Banago-Bredco, through its Bids and Awards Committee (BAC), invites suppliers/dealers to submit price quotation for each of the following item:

| Item No. | Description / Specification | Qty. | Unit | Approved Budget for the Contract |
| --- | --- | --- | --- | --- |
| 1) 2) 3) 4) 5) 6) 7) | SUPPLY, DELIVERY & COMMISSIONING OF CONSTRUCTION EQUIPMENT Welding Machine Heavy duty & Industrial type Power Voltage (V) – 220V-240V Digital Amp meter display With Voltage reduction device No-Load Voltage 75 Input Voltage Frequency (Hz) 50/60 Hz Current range (Amp) 500 or more Rated duty cycle - 60 Insulation class - F Protective class - IP21 Power Factor - 0.93 Usable electrodes (mm) 1.6-8.0 Portable Welding Machine Power Voltage – 220V – 240V Rated Input capacity (kVA0 6.3 Input Voltage Frequency (Hz) - 50/60 Hz Current range (Amp) 300 or more Rated duty cycle - 60 Insulation class – F Protective class IP21 Rated input voltage – 220-240V Power factor - 0.93 Net weight (KG) – 4.9 Usable electrodes (mm) 1.6-4.0 Clamp Tester/Meter with Accessories Digital Clamp Multimeter - Badwidth 50-400HZ - Clamp Diameter/conductor size 25mm/ 10 X 30mm or more - Size/mass H187 X W50 X D29mm/ 210g or more Electric Bar Cutter/Cut Off Machine - Cutting fence - Spark deflector for safety - Resistant steel base - Cutting capacity at rectangle - 100 x 196mm Cutting capacity at square – 119 x 119mm Cutting capacity at L-profile – 130 x 130mm Tool dimensions (width x length x height) – 256 x 520 x 400 mm Cutting disc diameter – 355mm Cutting disc bore – 25.4mm Weight – 15 kg Rated Input power – 2,200W Telescopic Ladder - Fiberglass rails in safety orange - Quicklatch rung lock - Outside slide guides - 10-17 Rungs / 20Ft or more - Heavy duty / self-aligning swivel Safety feet with steel ice plate Maximum Load 150g or more Pressure Washer with Accessories - 90bar 1300psi High Pressure washer - Electric water cleaner pump hose - Hose Length 10M or more with handle - Motor power : 1200W - 2HP Copper Oxygen & Acetylene Tank With Welding and cutting outfit - G150-60-540R Oxygen Regulator - G150-15-200R Acetylene Regulator - CA1350 Cutting Attachment - 100FC Torch Handle - MC Acetylene Bottle - 20 cu/ ft. Oxygen Bottle - 12.5” x 3/16” Grade R Twin Hose - 1-W-1 Welding Nozzle - 0-3-101 Cutting Tip - Striker - Goggles - Cylinder Wrench with Chain - Rugged molded plastic carrying case | 1 1 1 1 1 1 1 | Unit Unit Unit Unit Unit Unit Unit |  |

*Inclusive of 12% VAT

- Delivery Period				 :	Within Ten (10) calendar days from receipt of

Applicable Purchase Order (PO)

- Approved Budget for the Contract (ABC):	P 148,000.00

- Deadline for Submission of RFQ	            :           12:00 NN, November 18, 2019

- Opening of Sealed Canvass		:	1:00 PM, November 18, 2019

Procurement will be conducted in consonance with Section 53.9 (Small Value Procurement) of the Revised Implementing Rules and Regulations Part A (IRR-A) of the Republic Act 9184, otherwise known as the: Government Procurement Reform Act”.  Only sealed bids/canvass from eligible supplier/s will be opened and a Purchased Order will only be awarded to the Lowest Calculated and Responsive Bidder for each specific item who is determined as such during post-qualification.

Request for Quotation must be submitted in a sealed envelope together with the following documents:

- Certified true copy of Valid & Current Mayor’s Permit

- Certified true copy of Valid PhilGeps Registration

- Certified true copy of Latest Income/Business Tax Return, and

- Notarized Omnibus Sworn Statement.

The sealed envelope shall be addressed to

ENGR. RICHIE A VILLASANA

Chairperson, Bids and Awards Committee

Philippine Ports Authority, PMO – NBB

Banago Port, Brgy. Banago, Bacolod City

Interested bidders may obtain further information regarding RFQ Form from Zedric B. Turtogo or Mona Liza G. Villaran, BAC Secretariat at Banago Port, Brgy. Banago, Bacolod City during regular office hours. For further information, please refer to   Tel #: (034)441-1225/  441-1041/ 441-3124.

(SGD)

RICHIE A. VILLASANA

Chairperson, Bids and Awards Committee